Open Geospatial Consortium

Submission Date: 2014-11-25

License Agreement

Permission is hereby granted by the Open Geospatial Consortium, (“Licensor”), free of charge and subject to the terms set forth below, to any person obtaining a copy of this Intellectual Property and any associated documentation, to deal in the Intellectual Property without restriction (except as set forth below), including without limitation the rights to implement, use, copy, modify, merge, publish, distribute, and/or sublicense copies of the Intellectual Property, and to permit persons to whom the Intellectual Property is furnished to do so, provided that all copyright notices on the intellectual property are retained intact and that each person to whom the Intellectual Property is furnished agrees to the terms of this Agreement.

If you modify the Intellectual Property, all copies of the modified Intellectual Property must include, in addition to the above copyright notice, a notice that the Intellectual Property includes modifications that have not been approved or adopted by LICENSOR.

THIS LICENSE IS A COPYRIGHT LICENSE ONLY, AND DOES NOT CONVEY ANY RIGHTS UNDER ANY PATENTS THAT MAY BE IN FORCE ANYWHERE IN THE WORLD. THE INTELLECTUAL PROPERTY IS PROVIDED “AS IS”, WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NONINFRINGEMENT OF THIRD PARTY RIGHTS. THE COPYRIGHT HOLDER OR HOLDERS INCLUDED IN THIS NOTICE DO NOT WARRANT THAT THE FUNCTIONS CONTAINED IN THE INTELLECTUAL PROPERTY WILL MEET YOUR REQUIREMENTS OR THAT THE OPERATION OF THE INTELLECTUAL PROPERTY WILL BE UNINTERRUPTED OR ERROR FREE. ANY USE OF THE INTELLECTUAL PROPERTY SHALL BE MADE ENTIRELY AT THE USER’S OWN RISK. IN NO EVENT SHALL THE COPYRIGHT HOLDER OR ANY CONTRIBUTOR OF INTELLECTUAL PROPERTY RIGHTS TO THE INTELLECTUAL PROPERTY BE LIABLE FOR ANY CLAIM, OR ANY DIRECT, SPECIAL, INDIRECT OR CONSEQUENTIAL DAMAGES, OR ANY DAMAGES WHATSOEVER RESULTING FROM ANY ALLEGED INFRINGEMENT OR ANY LOSS OF USE, DATA OR PROFITS, WHETHER IN AN ACTION OF CONTRACT, NEGLIGENCE OR UNDER ANY OTHER LEGAL THEORY, ARISING OUT OF OR IN CONNECTION WITH THE IMPLEMENTATION, USE, COMMERCIALIZATION OR PERFORMANCE OF THIS INTELLECTUAL PROPERTY.

This license is effective until terminated. You may terminate it at any time by destroying the Intellectual Property together with all copies in any form. The license will also terminate if you fail to comply with any term or condition of this Agreement. Except as provided in the following sentence, no such termination of this license shall require the termination of any third party end-user sublicense to the Intellectual Property which is in force as of the date of notice of such termination. In addition, should the Intellectual Property, or the operation of the Intellectual Property, infringe, or in LICENSOR’s sole opinion be likely to infringe, any patent, copyright, trademark or other right of a third party, you agree that LICENSOR, in its sole discretion, may terminate this license without any compensation or liability to you, your licensees or any other party. You agree upon termination of any kind to destroy or cause to be destroyed the Intellectual Property together with all copies in any form, whether held by you or by any third party.

Except as contained in this notice, the name of LICENSOR or of any other holder of a copyright in all or part of the Intellectual Property shall not be used in advertising or otherwise to promote the sale, use or other dealings in this Intellectual Property without prior written authorization of LICENSOR or such copyright holder. LICENSOR is and shall at all times be the sole entity that may authorize you or any third party to use certification marks, trademarks or other special designations to indicate compliance with any LICENSOR standards or specifications. This Agreement is governed by the laws of the Commonwealth of Massachusetts. The application to this Agreement of the United Nations Convention on Contracts for the International Sale of Goods is hereby expressly excluded. In the event any provision of this Agreement shall be deemed unenforceable, void or invalid, such provision shall be modified so as to make it valid and enforceable, and as so modified the entire Agreement shall remain in full force and effect. No decision, action or inaction by LICENSOR shall be construed to be a waiver of any rights or remedies available to it.

None of the Intellectual Property or underlying information or technology may be downloaded or otherwise exported or reexported in violation of U.S. export laws and regulations. In addition, you are responsible for complying with any local laws in your jurisdiction which may impact your right to import, export or use the Intellectual Property, and you represent that you have complied with any regulations or registration procedures required by applicable law to make this license enforceable.

Suggested additions, changes and comments on this document are welcome and encouraged. Such suggestions may be submitted using the online change request form on OGC web site: http://portal.opengeospatial.org/public_ogc/change_request.php

Contents

TOC \o "1-2" \h \z \u   Copyright notice .     PAGEREF _Toc936559534 \h  1

Note .     PAGEREF _Toc704871609 \h  1

License Agreement .     PAGEREF _Toc221924087 \h  1

Notice .     PAGEREF _Toc456546006 \h  1

I. Abstract .     PAGEREF _Toc152791508 \h  1

II. Keywords .     PAGEREF _Toc310443626 \h  1

III. Preface .     PAGEREF _Toc765562272 \h  1

IV. Security considerations .     PAGEREF _Toc030526662 \h  1

V. Submitting Organizations .     PAGEREF _Toc182542310 \h  1

VI. Submitters .     PAGEREF _Toc833041733 \h  1

VII. Introduction .     PAGEREF _Toc418405438 \h  1

1. Scope .     PAGEREF _Toc074758846 \h  1

2. Conformance .     PAGEREF _Toc780489823 \h  1

3. Normative references .     PAGEREF _Toc269972322 \h  1

4. Terms and definitions .     PAGEREF _Toc035779734 \h  1

5. Conventions .     PAGEREF _Toc115462304 \h  1

5.1. Abbreviated terms .     PAGEREF _Toc495351062 \h  1

5.2. Use of the Term “Process” .     PAGEREF _Toc519431543 \h  1

5.3. UML Notation .     PAGEREF _Toc142145288 \h  1

5.4. Namespace Conventions .     PAGEREF _Toc510906730 \h  1

6. WPS Conceptual Model .     PAGEREF _Toc666485800 \h  1

6.1. Service Discovery .     PAGEREF _Toc445802962 \h  1

6.2. Service Capabilities .     PAGEREF _Toc159866871 \h  1

7. WPS Native Process Model .     PAGEREF _Toc857592187 \h  1

7.1. Common Description Type .     PAGEREF _Toc844268847 \h  1

7.2. Data Description Structure .     PAGEREF _Toc775022811 \h  1

8. WPS Native Process Model Encoding .     PAGEREF _Toc677008867 \h  1

8.1. XML Schema Implementation .     PAGEREF _Toc724230322 \h  1

8.2. Plain Text Encoding for LiteralData and BoundingBoxData Values .     PAGEREF _Toc811275086 \h  1

9. Common WPS Service Model .     PAGEREF _Toc806576934 \h  1

9.1. Overview of WPS Core Operations .     PAGEREF _Toc588821005 \h  1

9.2. Data Transmission .     PAGEREF _Toc699554960 \h  1

Annex A (normative) Abstract Test Suite .     PAGEREF _Toc733948020 \h  1

A.1. Basic WPS (Conformance Class) .     PAGEREF _Toc938832498 \h  1

Annex B (informative) XML Examples .     PAGEREF _Toc917995537 \h  1

B.1. Data Types .     PAGEREF _Toc172736754 \h  1

Bibliography .     PAGEREF _Toc273248094 \h  1

Copyright notice

Copyright © 2015 Open Geospatial Consortium

To obtain additional rights of use, visit http://www.ogc.org/legal/

Note

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. The Open Geospatial Consortium shall not be held responsible for identifying any or all such patent rights.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the standard set forth in this document, and to provide supporting documentation.

Notice

This document is an OGC Member approved international standard. This document is available on a royalty free, non-discriminatory basis. Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# I.  Abstract

In many cases geospatial or location data, including data from sensors, must be processed before the information can be used effectively. The OGC Web Processing Service (WPS) Interface Standard provides a standard interface that simplifies the task of making simple or complex computational processing services accessible via web services. Such services include well-known processes found in GIS software as well as specialized processes for spatio-temporal modeling and simulation. While the OGC WPS standard was designed with spatial processing in mind, it can also be used to readily insert non-spatial processing tasks into a web services environment.

# II.  Keywords

The following are keywords to be used by search engines and document catalogues.

TBD, geoprocessing, ogcdoc, OGC document, processes, processing, WPS

# III.  Preface

This standard is a continuation of WPS 1.0, a standard for web-based processing of geospatial data. It incorporates a range of change requests that have been submitted since the release of WPS 1.0 and further follows the OGC standard for modular specifications [OGC 08-131r3].

In contrast to the prior version, WPS 2.0 provides a core conceptual model that may be used to specify a WPS in different architectures such as REST or SOAP.

The WPS process model has been encapsulated into separate requirements and conformance classes, so it may be used independently from WPS servers in process catalogs and metadata records. The expressive power of process descriptions has been enhanced by permitting structured (or nested) inputs and outputs. The concept of process profiles has been clarified and extended to support process descriptions at different levels of abstraction.

Conversely, the process model itself has been largely decoupled from the WPS protocol, allowing the use of other domain-specific descriptions of processes, e.g. those defined in SensorML, and to execute them on a WPS server.

This specification also provides a Basic WPS conformance class that comprises the synchronous and asynchronous execution protocol, the WPS process model, and implements HTTP/POST+XML and HTTP/GET+KVP encodings.

Future work will target the definition of process interfaces for common processes based on the process model conformance class. Such profiles will encourage the development of well-defined, reliable, interoperable and exchangeable process implementations.

If OGC baseline and related specifications should further progress towards REST-oriented interfaces, the development of a REST-oriented WPS interface standard should be considered.

# IV.  Security considerations

No security considerations have been made for this document.

# V.  Submitting Organizations

The following organizations submitted this Document to the Open Geospatial Consortium (OGC):

TU Dresden

52°North

Intergraph Corporation

Image Matters LLC

CRP Henri Tudor

Airbus Defence and Space

# VI.  Submitters

| Name | Representing | OGC member |
| --- | --- | --- |
| Matthias Müller | TU Dresden | Yes |
| Benjamin Pross | 52°North | Yes |
| Stan Tillman | Intergraph Corporation | Yes |
| Jeff Yutzler | Image Matters LLC | Yes |
| Luís de Sousa | CRP Henri Tudor | Yes |
| Arnaud Cauchy | Airbus Defence & Space | Yes |

# VII.  Introduction

The WPS standard provides a robust, interoperable, and versatile protocol for process execution on web services. It supports both immediate processing for computational tasks that take little time and asynchronous processing for more complex and time consuming tasks. Moreover, the WPS standard defines a general process model that is designed to provide an interoperable description of processing functions. It is intended to support process cataloguing and discovery in a distributed environment.

OGC® WPS 2.0.2 Interface Standard Corrigendum 2

# 1.  Scope

This document specifies the interface to a general purpose Web Processing Service (WPS). A WPS is a web service that enables the execution of computing processes and the retrieval of metadata describing their purpose and functionality. Typically, these processes combine raster, vector, and/or coverage data with well-defined algorithms to produce new raster, vector, and/or coverage information.

The WPS protocol supports both synchronous and asynchronous execution of processes. Synchronous execution may be used in simple and quick computation scenarios, where the data processing takes little to almost no time. Asynchronous processing is particularly well suited for complex computation scenarios which may take significant time.

The specification uses a core and extensions model to organize its features:

A core conceptual model, defining basic requirements for a web based processing service,

A process model to support the description and discovery of processes on the web,

A basic data model that supports arbitrary (standard or non-standard) data formats for inputs and outputs,

A WPS service model and encoding based on OGC baseline standards, and

A Dismiss extension to allow clients to terminate asynchronous processing jobs.

# 2.  Conformance

Conformance with this standard shall be checked using all the relevant tests specified in Annex A (normative) of this document. The framework, concepts, and methodology for testing, and the criteria to be achieved to claim conformance are specified in the OGC Compliance Testing Policies and Procedures and the OGC Compliance Testing web site.

Table 1 — Conformance classes related to WPS 2.0

| Conformance Class | Description | Clause |
| --- | --- | --- |
| http://www.opengis.net/spec/WPS/2.0/conf/service/profile/ basic-wps | Basic WPS service profile | Annex A.1 |
| http://www.opengis.net/spec/WPS/2.0/conf/service/ synchronous-wps | Synchronous WPS |  |
| http://www.opengis.net/spec/WPS/2.0/conf/service/ asynchronous-wps | Asynchronous WPS |  |
| http://www.opengis.net/spec/WPS/2.0/conf/ process-model-encoding | WPS process model encoding |  |
| http://www.opengis.net/spec/WPS/2.0/conf/service/ dismiss-extension | Dismiss extension |  |

# 3.  Normative references

The following documents are referred to in the text in such a way that some or all of their content constitutes requirements of this document. For dated references, only the edition cited applies. For undated references, the latest edition of the referenced document (including any amendments) applies.

Arliss Whiteside Jim Greenwood: OGC 06-121r9, OGC Web Service Common Implementation Specification. Open Geospatial Consortium (2010). https://portal.ogc.org/files/?artifact id=38867.

Policy SWG: OGC 08-131r3, The Specification Model — Standard for Modular specifications. Open Geospatial Consortium (2009). https://portal.ogc.org/files/?artifact id=34762&version=2.

A. Phillips, M. Davis: IETF RFC 4646, Tags for Identifying Languages. (2006). https://www.rfc-editor.org/info/rfc4646.

T. Berners-Lee, R. Fielding, L. Masinter: IETF RFC 3986, Uniform Resource Identifier (URI): Generic Syntax. (2005). https://www.rfc-editor.org/info/rfc3986.

ISO: ISO 8601:2004, Data elements and interchange formats — Information interchange — Representation of dates and times. International Organization for Standardization, Geneva (2004). https://www.iso.org/standard/40874.html.

W3C xmlschema-2, XML Schema Part 2: Datatypes Second Edition. https://www.w3.org/TR/xmlschema-2/.

# 4.  Terms and definitions

This document uses the terms defined in OGC Policy Directive 49, which is based on the ISO/IEC Directives, Part 2, Rules for the structure and drafting of International Standards. In particular, the word “shall” (not “must”) is the verb form used to indicate a requirement to be strictly followed to conform to this document and OGC documents do not use the equivalent phrases in the ISO/IEC Directives, Part 2.

This document also uses terms defined in the OGC Standard for Modular specifications (OGC 08-131r3), also known as the ‘ModSpec’. The definitions of terms such as standard, specification, requirement, and conformance test are provided in the ModSpec.

For the purposes of this document, the following additional terms and definitions apply.

This document uses the terms defined in Sub-clause 5.3 of [OGC 06-121r9], which is based on the ISO/IEC Directives, Part 2, Rules for the structure and drafting of International Standards. In particular, the word “shall” (not “must”) is the verb form used to indicate a requirement to be strictly followed to conform to this standard.

For the purposes of this document, the following additional terms and definitions apply.

4.1. dataset

collection of data, published or curated by a single agent, and available for access or download in one or more formats

Note 1 to entry: The use of ‘collection’ in the definition from [DCAT] is broader than the use of the term collection in this specification.

[SOURCE: W3C vocab-dcat]

4.2. distribution

represents an accessible form of a dataset

Example

a downloadable file, an RSS feed or an API.

[SOURCE: W3C vocab-dcat]

4.3. feature

characteristic ADMITTED

character DEPRECATED

abstraction of real world phenomena

Note 1 to entry: For those unfamiliar with the term ‘feature’, the explanations on Spatial Things, Features and Geometry in the W3C/OGC Spatial Data on the Web Best Practice document provide more detail.

[SOURCE: ISO 19101-1:2014, modified – added alternative term for “characteristic” and deprecated term “character”.]

4.4. Process

A process p is a function that for each input returns a corresponding output

μ:X→Y

where  X   denotes the domain of arguments x and  Y   denotes the co-domain of values y. Within this specification, process arguments are referred to as process inputs and result values are referred to as process outputs. Processes that have no process inputs represent value generators that deliver constant or random process outputs.

4.5. Process description

A process description is an information model that specifies the interface of a process. A process description is used for a machine-readable description of the process itself but also provides some basic information about the process inputs and outputs.

# 5.  Conventions

This section provides details and examples for any conventions used in the document. Examples of conventions are symbols, abbreviations, use of XML schema, or special notes regarding how to read the document.

## 5.1.  Abbreviated terms

| GML | Geography Markup Language |
| --- | --- |
| GRS | Coordinate Reference System |
| HTTP | Hypertext Transfer Protocol |
| ISO | International Organization for Standardization |
| KVP | Keyword Value Pair |
| MIME | Multipurpose Internet Mail Extensions |
| OGC | Open Geospatial Consortium |
| UML | Unified Modeling Language |
| URI | Universal Resource Identifier |
| URL | Uniform Resource Locator |
| WPS | Web Processing Service |
| XML | Extensible Markup Language |

## 5.2.  Use of the Term “Process”

The term process is one of the most used terms both in the information and geosciences domain. If not stated otherwise, this specification uses the term process as an umbrella term for any algorithm, calculation or model that either generates new data or transforms some input data into output data as defined in Clause 4.4.

## 5.3.  UML Notation

Unified Modeling Language (UML) static structure diagrams appearing in this specification are used as described in section 5.2 of OGC06-121r9. Further, the following conventions hold:

UML elements having a package name of “OWS Common” are those defined in the UML model of OWS Common [OGC 06-121r9].

UML data type Any is used here as an equivalence to XML’s xsd:any.

UML elements not qualified with a package name are those defined in this standard.

The UML model data dictionary is specified herein in a series of tables. The contents of the columns in these tables are described in section 5.5 of [OGC 06-121r9]. The contents of these data dictionary tables are normative, including any table footnotes.

## 5.4.  Namespace Conventions

The following namespaces are used in this document. The prefix abbreviations used constitute conventions used here, but are not normative. The namespaces to which the prefixes refer are normative, however.

| Prefix | Namespace URI | Description |
| --- | --- | --- |
| ows | http://www.opengis.net/ows/2.0 | OWS Common 2.0 XML Schema |
| xlink | http://www.w3.org/1999/xlink | Definitions for XLINK |
| xml | http://www.w3.org/XML/1998/namespace | XML (required for xml:lang) |
| xs | http://www.w3.org/2001/XMLSchema | XML Schema |

# 6.  WPS Conceptual Model

The WPS service model defines basic properties of any WPS server. A WPS server is a web service that provides access to pre-defined processes and provides job control operations to instantiate, control and monitor processing jobs (Figure 1).

Figure 1 — Artifacts of the WPS service model

| Requirements class 1 |
| --- |
| Obligation | requirement |
| Target type | Derived information model, encoding, and software implementation |
| Requirement | Requirement 1-1 |
| Requirement | Requirement 1-2 |
| Recommendation | Recommendation 1-1 |
| Requirement | Requirement 1-3 |
| Requirement | Requirement 1-4 |
| Requirement | Requirement 1-5 |
| Requirement | Requirement 1-6 |

## 6.1.  Service Discovery

Any WPS server shall be self-contained, i.e. provide an initial endpoint that can be used by a WPS client to determine the server’s capabilities.

| Requirements class 2 |
| --- |
| Obligation | requirement |
| Target type | Derived information model, encoding, and software implementation |
| Requirement | Requirement 2-1 |
| Requirement | Requirement 2-2 |
| Requirement | Requirement 2-3 |

## 6.2.  Service Capabilities

The basic capabilities of any WPS server fall into two categories: The first category comprises capabilities for process discovery and retrieval of process descriptions. The second category comprises capabilities to manage and monitor processing jobs.

Since the processes provided by a WPS server may have different degrees of complexity, the server shall indicate the allowed job control capabilities mode per process offering.

Further service capabilities, i.e. for secure communication and user authentication may be provided with the service but are neither covered nor restricted by this specification as long as they do not alter or change the semantics of other job control capabilities.

| Requirements class 3 |
| --- |
| Obligation | requirement |
| Target type | Derived information model, encoding, and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model/process |
| Requirement | Requirement 3-1 |
| Requirement | Requirement 3-2 |
| Requirement | Requirement 3-3 |
| Requirement | Requirement 3-4 |

# 7.  WPS Native Process Model

This section describes the information model of requirements. The corresponding XML and plain text encodings are specified in Clause 8.

| Requirements class 4 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model/process |
| Requirement | Requirement 4-1 |
| Requirement | Requirement 4-2 |
| Requirement | Requirement 4-3 |
| Requirement | Requirement 4-4 |
| Requirement | Requirement 4-5 |

## 7.1.  Common Description Type

Descriptive elements of processes, inputs and outputs are derived from the BasicIdentificationType provided by OWS Common (Figure 2). Other descriptive information shall be recorded in the Metadata element in the form of simple links with an appropriate role identifier.

| Requirements class 5 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model/process |
| Dependency | OWS Common 2.0 — BasicDescriptionType |
| Requirement | Requirement 5-1 |
| Requirement | Requirement 5-2 |
| Requirement | Requirement 5-3 |
| Requirement | Requirement 5-4 |
| Requirement | Requirement 5-5 |

Figure 2 — DescriptionType for processes, process inputs and process outputs UML class diagram

Table 2 — Properties of the DescriptionType structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| Title | Title of the process, input, and output. Normally available for display to a human. | ows:Title | One (mandatory) |
| Abstract | Brief narrative description of a process, input, and output. Normally available for display to a human. | ows:Abstract | Zero or one (optional) Include when available and useful. |
| Keywords | Keywords that characterize a process, its inputs, and outputs. | ows:Keywords | Zero or more (optional) Include when available and useful. |
| Identifier | Unambiguous identifier of a process, input, and output. | ows:Identifier Value is a URI or HTTP-URIa | One (mandatory) |
| Metadata | Reference to additional metadata about this item. | ows:Metadata Allowed values are specified in Table 3. | Zero or more (optional) |
| a Additional content such as separate code space and version attributes in the Identifier element are not allowed. |

Table 3 — Properties of the Metadata structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| Title | Title of the documentation. Normally available for display to a human. | Character String | One (mandatory) |
| Link type | Type of the xlink, fixed to simple. | Character String, fixed to “simple”. | One (mandatory) |
| Role | Role identifier, indicating the role of the linked document. | HTTP-URI | One (mandatory) |
| href | Reference to a documentation site for a process, input, or output. | HTTP-URI | One (mandatory) |

## 7.2.  Data Description Structure

The DataDescription structure contains basic properties for defining data inputs and outputs, including mimetype, encoding and schema. These properties specify supported formats for input and output data of computing processes. Any input or output item may support multiple formats, one of which is the default format. Processes may require that an input or output data set does not exceed a certain data volume.

| Requirements class 6 |
| --- |
| Obligation | requirement |
| Target type | Derived information model, encoding, and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model/process |
| Requirement | Requirement 6-1 |
| Requirement | Requirement 6-2 |

Figure 3 — DataDescription and supported formats UML class diagram

Table 4 — Format properties

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| mimetype | Media type of the data. | Character String | One (mandatory) |
| encoding | Encoding procedure or character set of the data (e.g. raw or base64) | Character String, fixed to “simple”. | One (mandatory) |
| schema | Identification of the data schema. | HTTP-URI | One (mandatory) |
| maximumMegabytes | The maximum size of the input data, in megabytes. | Integer | Zero or one (optional) |
| default | Indicates that this format is the default format.a | Boolean | Zero or one (conditional)a,b |
| a Defaults to FALSE if omitted. b One of the formats included in the DataDescription structure shall have the attribute “default” set to “true”. |

# 8.  WPS Native Process Model Encoding

## 8.1.  XML Schema Implementation

This section specifies the XML encoding of the elements of the WPS native process model. The referred XML schema elements are provided by the associated schema package delivered with this standard and located at http://schemas.opengis.net/wps/2.0/.

| Requirements class 7 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 7-1 |
| Requirement | Requirement 7-2 |
| Requirement | Requirement 7-3 |

### 8.1.1.  Data Types

The XML encoding of data types defines encoding rules for ComplexData, LiteralData, BoundingBoxData as well as their values.

Examples for data type encodings are listed in Annex B.1.

| Requirements class 8 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/complex-data |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/literal-data |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/bounding-box-data |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 8-1 |
| Requirement | Requirement 8-2 |

### 8.1.2.  Process Description

This clause specifies the XML encoding for the Process description.

| Requirements class 9 |
| --- |
| Obligation | requirement |
| Target type | Derived software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/description |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 9-1 |
| Requirement | Requirement 9-2 |

### 8.1.3.  Generic Process

This clause specifies the XML encoding for the GenericProcess.

| Requirements class 10 |
| --- |
| Obligation | requirement |
| Target type | Derived software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/profile/generic |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 10-1 |
| Requirement | Requirement 10-2 |

## 8.2.  Plain Text Encoding for LiteralData and BoundingBoxData Values

This clause specifies the plain text encoding of data types for literal and bounding box data values.

| Requirements class 11 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/complex-data |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/literal-data |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/native-process/model/datatypes/bounding-box-data |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 11-1 |
| Requirement | Requirement 11-2 |

Literal values - BNF schema:

literalvalue   = value *1("@datatype=" datatype) *1("@uom=" uom)

value          = 1*VCHAR

datatype  = URI

uom       = URI

Literal values - Example:

70@datatype=http://www.w3.org/2001/XMLSchema#integer@uom=meter

BoundingBox values - BNF schema:

bbox      = lc_coords "," uc_coords ["," crs] ["," dimensions]

lc_coords = number ["," number]

uc_coords = number ["," number]

number         = 1*DIGIT["." 1*DIGIT]

crs       = 1*VCHAR

dimensions = 1*DIGIT

BoundingBoxData values - Examples:

51.9,7.0,53.0,8.0,EPSG:4326

51.9,7.0,53.0,8.0,http://www.opengis.net/def/crs/EPSG/0/4258

# 9.  Common WPS Service Model

A Web Processing Service consists of processes and service operations. By definition, processes represent the computational functionality of a WPS, while service operations are used to interact with the WPS and in particular to use the service’s process offerings.

| Requirements class 12 |
| --- |
| Obligation | requirement |
| Target type | Software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model |
| Dependency | OWS Common 2.0 |
| Requirement | Requirement 12-1 |
| Requirement | Requirement 12-2 |
| Requirement | Requirement 12-3 |
| Requirement | Requirement 12-4 |
| Requirement | Requirement 12-5 |
| Requirement | Requirement 12-6 |
| Requirement | Requirement 12-7 |
| Requirement | Requirement 12-8 |
| Requirement | Requirement 12-9 |
| Requirement | Requirement 12-10 |

## 9.1.  Overview of WPS Core Operations

The WPS interface specified in this section supports retrieval and execution of processes for geospatial computation. For that purpose, the WPS service model specifies the following operations that may be invoked by a WPS client and performed by a WPS server:

GetCapabilities — This operation allows a client to request information about the server’s capabilities and processes offered.

DescribeProcess — This operation allows a client to request detailed metadata on selected processes offered by a server.

Execute — This operation allows a client to execute a process comprised of a process identifier, the desired data inputs and the desired output formats.

GetStatus — This operation allows a client to query status information of a processing job (conditional).

GetResult — This operation allows a client to query the results of a processing job (conditional).

During a sequence of WPS requests, a client should first issue a GetCapabilities request to the server to obtain an up-to date listing of available processes. Then, it may issue a DescribeProcess request to find out more details about particular processes offered, including the supported data formats. To run a process with the desired input data, a client will issue an Execute request (Figure 4).

The operations GetStatus and GetResult are used in conjunction with asynchronous execution. If a WPS server offers synchronous process execution only, these operations may not be implemented. Detailed guidance is provided by the corresponding profiles and conformance classes.

Figure 4 — Common sequence of WPS operations UML sequence diagram

## 9.2.  Data Transmission

Data exchange between WPS clients and servers requires an agreement on the general data exchange patterns and suitable communication protocols. Data may be sent to (received from) a WPS in two distinct ways: (1) by reference (using HTTP/GET or HTTP/POST), and (2) by value. Clients may send input data in either fashion. Output data may be requested in any fashion declared by the data transmission options defined for the process offering. Typically, large data inputs and outputs are delivered by reference.

| Requirements class 13 |
| --- |
| Obligation | requirement |
| Target type | Derived encoding and software implementation |
| Dependency | http://www.opengis.net/spec/WPS/2.0/req/conceptual-model |
| Requirement | Requirement 13-1 |

Figure 5 — Input and output data transmission structures UML class diagram

Table 5 — Parts of the inline Data structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| mimetype | See Table 6 — Properties of the DataEncodingAttributes structure. |
| encoding |
| schema |
| (any)a | The actual input or output data. | Any type and value | One (mandatory) |
| a The data is embedded here as part of the Data element, in the mimeType, encoding, and schema indicated by the first three parameters if they exist, or by the relevant defaults. |

Table 6 — Properties of the DataEncodingAttributes structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| mimetype | MimeType of the data. | Character String | One (mandatory) |
| encoding | Well-known encoding or character set of the data. | URI “raw” shall be used for plain binary data “base64” shall be used for base64 encoded data Character set identifiers (e.g. “UTF-8”) shall be used for text or CSV data. | Zero or one (conditional)a |
| schema | Identification of the data schema. | URI | Zero or one (conditional)a |
| a This shall be provided if: 1) the process data item supports multiple encodings / schemas, and 2) the data is not of the default encoding / schema, and 3a) the schema / encoding cannot be retrieved from the data itself, or 3b) the encoding / schema information is deeply buried inside the data (i.e. not part of some header) and requires significant parsing effort. |

Table 7 — Parts of the Reference structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| mimetype | See Table 6 — Properties of the DataEncodingAttributes structure. |
| encoding |
| schema |
| href | HTTP URI that points to the remote resource where the data may be retrieved. | HTTP URI | One (mandatory) |
| RequestBody | Request body element that is used for HTTP/POST requests to the above URL. If no request body is present, an HTTP/GET | Request should be used to retrieve the data. RequestBody structure, see Table 8. | Zero or one (optional) |

Table 8 — Parts of the RequestBody structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| Body | The contents of this element to be used as the body of the HTTP request message to be sent to the service identified in ../Reference/@href. For example, it could be an XML encoded WFS request using HTTP/POST. | Any type | Zero or one (conditional)a |
| BodyReference | Reference to a remote document to be used as the body of an HTTP/POST request message to the service identified in the href element in the Reference structure (Table 7). | BodyReference, see Table 9. | Zero or one (conditional)a |
| a One and only one of these items shall be included. |

Table 9 — Parts of the BodyReference structure

| Names | Definition | Data type and values | Multiplicity and use |
| --- | --- | --- | --- |
| href | HTTP URI that points to the remote resource where the request body may be retrieved. | HTTP URI | One (mandatory) |

Annex A

(normative)

# Abstract Test Suite

Tests and requirement identifiers below are relative to http://www.opengis.net/spec/WPS/2.0

## A.1.  Basic WPS (Conformance Class)

The OGC URI identifier of this conformance class is: http://www.opengis.net/spec/WPS/2.0/conf/service/profile/basic-wps

Example

Requirement A.1

conf/service/profile/basic-wps

Recommendation A.1

Verify that the server implements the Basic WPS conformance class.

Requirement A.2

Verify that the server implements the Synchronous WPS and/or the Asynchronous WPS conformance class. Verify that the requests and responses to a supported operation are syntactically correct. Verify that the service supports the Synchronous WPS Conformance class, the Asynchronous WPS Conformance class or both. Verify that all process offerings implement the native process model.

Annex B

(informative)

# XML Examples

## B.1.  Data Types

### B.1.1.  Complex Data Description

<wps:ComplexData>

<wps:Format mimeType="application/geotiff" encoding="raw"

default="true"/>

<wps:Format mimeType="application/geotiff" encoding="base64"/>

</wps:ComplexData>

### B.1.2.  Literal Data Description

<wps:LiteralData>

<wps:Format mimeType="text/plain" default="true"/>

<wps:Format mimeType="text/xml"/>

<LiteralDataDomain default="true">

<ows:AllowedValues>

<ows:Range>

<ows:MinimumValue>1</ows:MinimumValue>

<ows:MaximumValue>1000</ows:MaximumValue>

</ows:Range>

</ows:AllowedValues>

<ows:DataType

ows:reference="http://www.w3.org/2001/XMLSchema#float">float

</ows:DataType>

<ows:UOM>meters</ows:UOM>

<ows:DefaultValue>100</ows:DefaultValue>

</LiteralDataDomain>

<LiteralDataDomain>

<ows:AllowedValues>

<ows:Range>

<ows:MinimumValue>1</ows:MinimumValue>

<ows:MaximumValue>3000</ows:MaximumValue>

</ows:Range>

</ows:AllowedValues>

<ows:DataType

ows:reference="http://www.w3.org/2001/XMLSchema#float">float

</ows:DataType>

<ows:UOM>feet</ows:UOM>

</LiteralDataDomain>

</wps:LiteralData>

### B.1.3.  Literal data values

<LiteralValue

dataType=http://www.w3.org/2001/XMLSchema#double

uom="meter">

42.1

</LiteralValue>

<LiteralValue

dataType="http://www.w3.org/2001/XMLSchema#string">

ArableLand

</LiteralValue>

### B.1.4.  BoundingBox Data Description

<wps:BoundingBoxData>

<wps:Format mimeType="text/plain" default="true"/>

<wps:Format mimeType="text/xml"/>

<wps:SupportedCRS default="true">EPSG:4326</wps:SupportedCRS>

<wps:SupportedCRS>

http://www.opengis.net/def/crs/EPSG/0/4258

</wps:SupportedCRS>

</wps:BoundingBoxData>

### B.1.5.  BoundingBox Data Values

<ows:BoundingBox crs="EPSG:4326">

<ows:LowerCorner>51.9 7.0</ows:LowerCorner>

<ows:UpperCorner>53.0 8.0</ows:UpperCorner>

</ows:BoundingBox>

<ows:BoundingBox

crs="http://www.opengis.net/def/crs/EPSG/0/4258">

<ows:LowerCorner>51.9 7.0</ows:LowerCorner>

<ows:UpperCorner>53.0 8.0</ows:UpperCorner>

</ows:BoundingBox>

# Bibliography

[1]  ISO: ISO 19101, Geographic information — Reference model. International Organization for Standardization, Geneva https://www.iso.org/standard/26002.html.

[2]  W3C vocab-dcat, Data Catalog Vocabulary (DCAT). https://www.w3.org/TR/vocab-dcat/.

www.opengeospatial.org/cite

The dimensions attribute is included for compliance with the BoundingBox structure defined in OWS Common [OGC 06-121r9]. However, its use should be generally avoided since the number of dimensions is already part of the CRS definition and usually superfluous.

NOTE: Future extensions of this specification may introduce additional operations.

NOTE: A WPS server can change its offering at any time, in particular between a GetCapabilities, a subsequent DescribeProcess, and a subsequent Execute request. Any quality of service (QoS) guarantees are within the responsibilities of the service provider and not covered by this standard.